## Slide 1
(Experimenting with New Technologies)
Software Defined
with TF Mini Plus
Block
Detector

## Slide 7
Track 1
Track 2
Heisler
Shay
I have a layout I take to shows that has a loop with a hidden passing track. While the rest of the layout is DCC, this is analog. Using reed switches and relays, I have a Shay that comes from behind trees and brings loaded log cars to the logging camp. After it disappears behind the camp, a Heisler brings empties back to the woods.

## Slide 8
Track 1
Track 2
Heisler
Shay
Running analog, is simple. A reed switch at entry on track 1 closes a relay that sustains itself, and is a reversing switch to the loop. The trains go in opposite direction: the loaded one to the sawmill, the empties go from the mill back to the woods. A reed switch on track 2 releases the relay. A diode to each track stops the incoming train while the other train makes the trip. That all works beautifully, but I would like to do this with JMRI scripting.

## Slide 9
DC Power Supply
Rail A
Rail B
Relay
Track 1
Track 2
Heisler
Shay
Track 1
Track 2
Gap in Rail
Isolated section only powered for one travel direction as diode blocks polarity for the other
“At Point” Reed switch detectors activate polarity relay for one or the other direction: Arriving Shay starts Heisler and vice versa
Running analog, is simple. A reed switch at entry on track 1 closes a relay that sustains itself, and is a reversing switch to the loop. The trains go in opposite direction: the loaded one to the sawmill, the empties go from the mill back to the woods. A reed switch on track 2 releases the relay. A diode to each track stops the incoming train while the other train makes the trip. That all works beautifully, but I would like to do this with JMRI scripting.

## Slide 10
Heisler
Shay

## Slide 11
(Experimenting with New Technologies)
Hi Resolution
Block Detector II
with RFID

## Slide 13: Looking for…
Reliable detection of a car or locomotive
No modification of the axles
Information available right after powering up the layout
Hi resolution
Providing the exact location of the train within the block

## Slide 14
DC Power Supply
Rail A
Rail B
Relay
Track 1
Track 2
Heisler
Shay
Track 1
Track 2
Gap in Rail
Isolated section only powered for one travel direction as diode blocks polarity for the other
“At Point” detectors activate polarity relay for one or the other direction: Arriving Shay starts Heisler and vice versa

## Slide 15
Track 1
Track 2
Heisler
Shay
Software Defined Sensor
Track 1 Detection
Track 2 Detection

## Slide 16
ESP32 Wemos
MQTT
Broker
Gateway
Test
BlueBox
LocoNet over MQTT
Wired LocoNet
LED Strip
VL53L1X
Sensor
I2C Connection
MFRC522
Sensor
SPI Connection

## Slide 17
Sensor
Sensor Detection Area (Active Cone)
Undetected as Loco echo is too weak to be detected
Detected and measured as Loco reflects the beam well
10°
Adjustable Sensor Plate

## Slide 21
Track 1
Track 2
Heisler
Shay

## Slide 22
DC Power Supply
Rail A
Rail B
Relay
Track 1
Track 2
Heisler
Shay

## Slide 23
DC Power Supply
Rail A
Rail B
Relay
Track 1
Track 2
Heisler
Shay
Track 1
Track 2
Gap in Rail
Isolated section only powered for one travel direction as diode blocks polarity for the other

## Slide 24
DC Power Supply
Rail A
Rail B
Relay
Track 1
Track 2
Heisler
Shay
Track 1
Track 2
Gap in Rail
Isolated section only powered for one travel direction as diode blocks polarity for the other
“At Point” detectors activate polarity relay for one or the other direction: Arriving Shay starts Heisler and vice versa

## Slide 31
Relay inputs connected to IO Pins 11 and 12 …
…and DC input and track receptacles on the output

## Slide 36
LocoNet Interface Breakout board to IO pins 7 (Tx) and 8 (Rx) using jumper wire
Note: Modify Interface board for 5V signal level of Nano

## Slide 41
TF Mini Plus connected to IO pins 2&3 of the Nano

## Slide 47
Servo connected to IO pin 9 of the Nano

## Slide 50
Servo.h and LocoNet.h are not compatible. Compiling generates a lot of errors.

## Slide 51
PCA9685 module connected to analog pins 4 & 5 of the Nano, Servo connected to PCA9685 Port 0

## Slide 52
DIY DCC
16 Channel
Servo Decoder

## Slide 54
Track 1
Track 2
Heisler
Shay
Sensor
Potential viewing field of sensor at this position when it turns up to 180°
Track 1 Detection
Track 2 Detection
Potentially critical area: A train in this section might become invisible as it is behind another train located closer to the sensor

## Slide 68
Lidar Sensor
Polarity Relay
Rail Isolation
Diode (!)
Shay
Heisler

## Slide 72
Track 1
Track 2
Heisler
Shay
Sensor
Track 1 Detection
Track 2 Detection
Potentially critical area: A train in this section might become invisible as it is behind another train located closer to the sensor
Approaching Heisler blocks viewing field of Track 1 sensor, therefore the Shay becomes temporarily invisible

## Slide 73
Sensor
Sensor Detection Area (Active Cone)
Locomotive only crossing half of the cone leads to long reading

## Slide 74
Sensor
Sensor Detection Area (Active Cone)
Locomotive crossing entire cone, reading is precise

## Slide 75
Gear problems after 2+ hours of continuous operation

## Slide 77
57 |  |  |  |  |  |  | 
49 |  | 51 |  |  | 54 |  | 
41 | 42 | 43 |  |  | 46 | 47 | 
33 |  |  |  |  |  |  | 
25 |  |  |  |  |  |  | 
17 | 18 | 19 |  |  | 22 | 23 | 
9 |  | 11 |  |  | 14 |  | 
1 |  |  |  |  |  |  | 

## Slide 78: Summary

## Slide 79: Summary
A simple layout animation for two trains can easily be done using DC power, a relay and two “At Point” detectors to change the polarity

## Slide 80: Summary
A simple layout animation for two trains can easily be done using DC power, a relay and two “At Point” detectors to change the polarity
The suggested layout with a siding and two trains traveling in opposing directions seems simple but is complex enough to demonstrate more elaborated control concepts using DCC and JMRI scripting

## Slide 81: Summary
A simple layout animation for two trains can easily be done using DC power, a relay and two “At Point” detectors to change the polarity
The suggested layout with a siding and two trains traveling in opposing directions seems simple but is complex enough to demonstrate more elaborated control concepts using DCC and JMRI scripting
By using a Lidar sensor mounted on a servo it is possible to create a software defined universal occupancy sensor, at least for G scale, but I think it also would work for HO

## Slide 82: Summary
A simple layout animation for two trains can easily be done using DC power, a relay and two “At Point” detectors to change the polarity
The suggested layout with a siding and two trains traveling in opposing directions seems simple but is complex enough to demonstrate more elaborated control concepts using DCC and JMRI scripting
By using a Lidar sensor mounted on a servo it is possible to create a software defined universal occupancy sensor, at least for G scale, but I think it also would work for HO
With just two sensor locations, the readout frequency for each position is more than needed for train control. With more positions and wider angle there will be a slowdown.

## Slide 83: Summary
A simple layout animation for two trains can easily be done using DC power, a relay and two “At Point” detectors to change the polarity
The suggested layout with a siding and two trains traveling in opposing directions seems simple but is complex enough to demonstrate more elaborated control concepts using DCC and JMRI scripting
By using a Lidar sensor mounted on a servo it is possible to create a software defined universal occupancy sensor, at least for G scale, but I think it also would work for HO
With just two sensor locations, the readout frequency for each position is more than needed for train control. With more positions and wider angle there will be a slowdown.
Those cheap SG90 servos are not made for continuous operation. A higher quality drive train is needed to prevent frequent mechanical failure

## Slide 84
Tindie shop IoTT page: https://www.tindie.com/stores/tanner87661/
IoTT main page: https://myiott.org/
Github page for TF Mini plus library for Arduino: https://github.com/budryerson/TFMini-Plus
TF Mini plus: https://www.sparkfun.com/products/15179

## Slide 85
if (watching_this(video) == (useful || interesting))
{
please_click_like();
subscribe_channel():
hit_the_bell_icon();
leave_a_comment();
}

## Slide 86
if (watching_this(video) == (useful || interesting))
{
please_click_like();
}

## Slide 87
IoTT
Internet of Toy Trains